## Slide 1: IFS flight software
Maxime J Rizzo & GSFC IFS team

## Slide 2: Overview
Software has 2 roles:
  Extract a cleaned IFS detector image into a cube usable for wavefront sensing
  Update an existing calibration file using a monochromatic flatfield of psflets
    Uses simple centroiding for all psflets
    Least-squares fits the bulk x, y and theta shift of all psflets
    Calculate the dx,dy for all psflets resulting in the best fit correction
    Apply this dx, dy to all psflets on the Horne extraction calibration products
Memo on least squares fit:
for all spots i=0, …, n
Unknowns are the rotation matrix R and translation vector t, or unknown vector x = [s, c, tx, ty]T
Rewrite system of n equations under the form Ax=b and solve with lstsq or svd

## Slide 3: Extract
image
IFS 2d pixel array
Already cleaned and dark-subtracted
lamlist
List of desired wavelength slices in the output cube (nm)
calib
Calibration datafile
(crispy file)
extract1D
cube
sum
If False, runs 1D Horne extraction
If True, run 1D sum (default: False)
delt_y
Width of microspectra in cross-spectral direction in pixels (default: 5)
Required
Optional
Inputs
Function
Result
Extracts IFS frame into cube at desired wavelengths

## Slide 4: Update
data
IFS 2d pixel array of monochromatic spots
Already cleaned and dark-subtracted
monochromekey
Reference positions of psflets at calibration wavelength
halfsize
Half size of box for re-centroiding each psflet (default: 5)
update
dx, dy, snr
Offsets and snr for all psflets
apdiam
Diameter of photometric aperture
(default: 3)
snrthreshold
Discard psflets below this snr
(default: 10)
Required
Optional
Inputs
Function
Result
Finds dx, dy for each spots

## Slide 5: Post update
dx, dy, snr
Results of update function
old_monochromekey_file
Path to old monochrome key file
apply_update
Dx, Dy, sigx,sigy
Offsets and std for all psflets (Dx, Dy are 2D)
fitrot=True
If True, does a least squares fit on translation + rotation; if False, does only translation
Required
Optional
Inputs
Function
Result
Applies a wavelength calibration by creating new calibration files
Updated monochromekey and calibration file
old_calib_file
Path to old calibration file
new_monochromekey_file
Path to new monochrome key file
new_calib_file
Path to new calibration file

## Slide 6: Description of calibration files
monochrome_key: single slice of polychrome_key FITS from crispy
Contains X, Y information about the expected locations of the spots at a given wavelength
  Extension 0: wavelength
  Extension 1: x positions of the monochromatic spots for a given wavelength
  Extension 2: y positions of the monochromatic spots for a given wavelength
  Extension 3: boolean mask of good lenslets/psflets (if True, psflet is good)
calib: essential calibration products for Horne extraction
combination of PSFloc and PSFwidths for crispy
  Extension 0: lams: wavelengths at the center of each pixel for each microspectrum
  Extension 1: xindx: x coordinate for a given microspectrum and a given wavelength
  Extension 2: yindx: y coordinate (cross-spectral direction)
  Extension 3: nlam: number of valid wavelength bins in that microspectrum
  Extension 4: good: 2D Boolean mask indicating whether microspectrum is on detector
  Extension 5: psfwidths: 1-sigma widths of the PSFlets in pixels

## Slide 7
Y: cross-dispersion
direction
X: dispersion
direction
(xindx[ix,iy,0], yindx[ix,iy,0])
in detector pixel coordinates
(xindx[ix,iy,-1], yindx[ix,iy,-1])
in detector pixel coordinates
ix, iy = coordinates of this microspectrum in Lenslet array coordinates
xindx[ix,iy,:] is an array of integer coordinates which are matched to the wavelength array lams[ix,iy,:] (this reduces the number of interpolations during each extraction step)
yindx[ix,iy,:] is an array of floating point coordinates, as the spectrum can be sampled differently in the cross-dispersion direction
Because of this structure, the update step requires an interpolation to find the new set of integer pixels across the dispersion direction
delt_y

## Slide 8: Calibration procedure
Have monochrome_key and calib files ready
Take new monochromatic frame at the same wavelength as the monochrome_key file
Run update function
(optional: inspect/flag results)
If results acceptable:
  Select new names for calibration files
  run apply_update with new names
To verify that it worked, extract the new frame using the new calibration products
  Fit gaussian to verify that central wavelength is close to what you’d expect